## Slide 1
MOCK
Project
Report
28 Dec 2023

## Slide 2
OUTLINE
Input
2. Requirement
3. Connection diagram
4. Analyze requirement
5. Algorithm

## Slide 3
1. Input
  Hardware:
  - 2 buttons(onboard):
  + BT1(PTC12).
  + BT2(PTC13).
  - 1 8-digit seven-segment LED display.

## Slide 4
2. Requirement
  Write program: The Digital Clock
  SRS 1: After power on, display the time: 00-00-00 (date: 01.01.1971) SRS 2: Press Button 1 - SRS 2-1: Display the date - SRS 2-2: Display the time SRS 3: Press Button 2 - SRS 3-1: Turn off the display mode - SRS 3-2: Turn on the display mode SRS4: Setting date, time by UART serial communication SRS5: Use potentiometer to control the brightness of LED display(Opt)

## Slide 5
3. Connection diagram
8-digit seven-segment
LED display
S32K144EVB
BUTTON1
PTC12
PTB17
BUTTON2
PTC13
Connection Diagram
PTB14
PTB16
CLK
CS
DIN

## Slide 6
4. Analyze requirement
Time=00-00-00
  SRS 1: After power on, display the time: 00-00-00 (date: 01.01.1971)
Reset
Date=01.01.1972

## Slide 7
4. Analyze requirement
Display= {Time, Date }
  SRS 2: Press BT1
  SRS 2-1: Display the date (01.01.1972).
  SRS 2-2: Display the time (00-00-00).
Display the time
Display the date

## Slide 8
4. Analyze requirement
Mode= {ON, OFF }
  SRS 3: Press BT2
  SRS 3-1: Turn off the display mode.
  SRS 3-2: Turn off the display mode
Turn off
Turn on

## Slide 9
4. Analyze requirement
  SRS 4: Setting date, time by UART serial communication
Send string by UART
06201028102023
Display the time
Display the date

## Slide 10
5. Algorithm
Start
(1) Buttons Initialization
(2) Led display Initialization
(3) Display the time
(4) Send command to display Led
(5) Wait a second
(6) Processing the next mode
Main Task
10

## Slide 11
5. Algorithm
Begin Buttons Initialization
Enable clock for PORTC
Set pins as GPIO function
Disabled pull-up/pull-down
End Buttons Initialization
Set interrupt type
Set pins as input pin
Enable NVIC for Port C
(1) Buttons Initialization

## Slide 12
5. Algorithm
(2) LED display Initialization
11
Begin LED display Initialization
Setting TX/ Rx pin
Select source LPUART
Setting baud rate
End LED display Initialization
Setting frame
Enable interrupt
Enable transmitter and receiver
12

## Slide 13
5. Algorithm
Begin systick handler
Mode display = 1
T
F
Update time and date value
Send command display time
Send command display time
End systick handler
13

## Slide 14
5. Algorithm
Begin handle button
Value BTN2 = 1
Value BTN1 = 1
On display = 1
Send command to turn off display
T
End handle button
T
F
F
T
F
F
On display = 0
On display = 1
Send command to turn on display
Mode display = 1
Mode display = 0
Mode display = 1
T
14

## Slide 15
5. Algorithm
Begin UART RX interrupt
End UART RX interrupt
T
F
Rec_str[] = receive uart data
Index rec_str = 14
Index rec_str = 0
Update time and date value
15

## Slide 16
Thank you